## Slide 1
TOPIC 03 · HARDWARE
L2
Monitors, printers and storage
Output you can see and output you can hold, the two numbers that decide how fast a machine feels, and where your files actually live.
Lesson 2 of 4 · Two practice activities · Assessed in the Topic 03 Checkpoint
Notes: This lesson covers three of the four jobs: output, processing and storage.
It is also the lesson that unlocks the marked task at the end of the topic, because by the
end of it you will be able to read a laptop advert and say which numbers matter for a given
person and which ones are there to fill the page.

## Slide 2
OBJECTIVES
2
What you will be able to do
Five things you should be able to do without notes by the end of this lesson.
1
Compare display devices
Compare monitors and projectors on the specifications that actually matter.
2
Choose a printer
Choose between inkjet and laser for a stated purpose, and justify it on cost per page.
3
Softcopy vs hardcopy
Distinguish output you can only see from output you can hold.
4
Compare storage
Compare HDD, SSD, flash and cloud on speed, cost, capacity and durability.
5
Estimate capacity
Order the capacity units and estimate the storage a given set of files needs.
Five objectives — this is the longest lesson in the topic, and the one the marked task leans on.
Notes: Five objectives, which makes this the longest lesson in the topic. That is deliberate: the
marked task at the end asks you to compare three real machines against a budget, and four of
these five objectives are what you need to do it.
The fifth, estimating capacity, is the one people skip and then get wrong. Knowing that a
gigabyte is bigger than a megabyte is not the objective. Working out whether 256 gigabytes is
enough for a specific person is.

## Slide 3
OUTPUT
3
Getting results out
Monitors
The main output device. Size in inches, sharpness in resolution — 1920×1080 is standard.
Projectors
A monitor for a room. Brightness matters more than resolution in a lit classroom.
Printers
Hardcopy. Inkjet for photos and colour, laser for volume and crisp text.
Speakers
Audio output for media, alerts and accessibility tools like screen readers.
Headsets
Private audio output, usually paired with a microphone as an input device.
Actuators
Output that moves something: a printer motor, a vibration, a robot arm.
Softcopy is output you can only see on a screen. Hardcopy is output you can hold.
Notes: Six output devices, and two terms you must know for the quiz: softcopy and hardcopy.
Softcopy is output you can only see on a screen. Hardcopy is output you can hold. A printed
page is hardcopy; the same document on your monitor is softcopy.
Two details worth your attention. On projectors: brightness matters more than resolution in
a lit classroom. A very sharp, very dim projector is useless at eleven in the morning. On
printers: inkjet for photos and colour, laser for volume and crisp text — which is why the
school office has a laser and your aunt has an inkjet. The reason is cost per page: laser
toner is expensive to buy and cheap per page; inkjet cartridges are the other way round.
And actuators, the category people never think of as output. Output that moves something: a
printer motor, the vibration in your phone, a robot arm. If the computer caused it to happen
in the physical world, that is output.

## Slide 4
PROCESSING
4
The processor and its workbench
GHz
clock speed — how many billion basic operations the CPU handles each second
Cores
independent workers on one chip — four cores handle four tasks at once
GB
RAM capacity — how much work can stay open at the same time
RAM — the desk surface
Fast, temporary and volatile. Everything you have open sits here. Cut the power and it is gone instantly. Run short of it and the machine crawls.
Storage — the drawers
Slower, permanent and much larger. Files, programs and the operating system live here and survive being switched off.
Read a spec sheet as: how fast it thinks (GHz), how many things at once (cores), how much it can hold open (GB of RAM).
Notes: This is the slide that unlocks the marked task, so give it a minute.
Three numbers on every spec sheet. Gigahertz is clock speed — how many billion basic
operations per second. Cores are independent workers on one chip; four cores genuinely handle
four things at once. Gigabytes of RAM is how much work can stay open simultaneously.
Now the analogy that makes RAM and storage click, and it is worth memorising. RAM is the desk
surface: fast, and everything you are working on right now is spread across it. Storage is
the drawers: slower, much bigger, and things stay there when you go home.
Two consequences. Cut the power and the desk is swept clean instantly — that is why unsaved
work disappears. And if your desk is too small you spend all your time fetching things from
the drawers, which is exactly why a machine short of RAM crawls.

## Slide 5
STORAGE
5
Where files actually live
Capacity climbs in steps of roughly a thousand: KB → MB → GB → TB.
Hard drive (HDD)
Spinning magnetic disks. Cheap per gigabyte, large, but slower and easily damaged by a knock.
Solid-state (SSD)
No moving parts. Much faster and tougher, costs more per gigabyte. Standard in new laptops.
Flash memory
USB sticks and memory cards. Portable and convenient — and the easiest thing in the world to lose.
Optical discs
CDs and DVDs. Nearly obsolete: low capacity, and few new machines have a drive.
Cloud storage
Files kept on someone else's servers, reachable anywhere — as long as you have a connection.
Backups
A second copy in a different place. Not optional: drives fail without warning.
A photo is a few MB. A film is a few GB. A laptop drive is usually 256 GB to 1 TB.
Notes: Capacity climbs in steps of roughly a thousand: kilobyte, megabyte, gigabyte, terabyte. Fix
the sense of scale in your head with the line at the bottom — a photo is a few megabytes, a
film is a few gigabytes, a laptop drive is usually between 256 gigabytes and a terabyte.
The comparison that matters for your marked task is the first two. A hard drive is spinning
magnetic disks: cheap per gigabyte, large, but slow and easily killed by a knock. A
solid-state drive has no moving parts: much faster, much tougher, more expensive per
gigabyte. This is why a cheap laptop with an SSD often feels quicker than an expensive one
with a hard drive — and that is a Checkpoint question, so remember it.
Cloud storage is simply files on someone else's servers, with one condition: a connection.
And backups are the one non-negotiable item on the slide. Drives fail without warning.

## Slide 6
CAPACITY
6
How much storage does that actually need?
The units, in order
Each step is roughly a thousand times the one before.
KB → MB → GB → TB
The sizes worth memorising
A page of text is about 50 KB. The other three anchor figures are enough for any question you will be asked.
Photo ≈ 4 MB · Song ≈ 5 MB · Video ≈ 2 GB per hour
1
List and count
How many of each kind of file, not just "lots of photos".
2
Multiply
Count × typical size, one line per kind of file.
3
Convert once
Bring everything to the same unit before you add it up.
4
Add the backup
A second copy doubles the figure. Storage plans that forget this fail in month two.
Worked example: 500 photos ≈ 2 GB, 200 songs ≈ 1 GB, 10 hours of video ≈ 20 GB. Total ≈ 23 GB, so 64 GB with a backup copy — not 32 GB.
Notes: This slide is the fifth objective, and it is the one people lose marks on, because they know
the units and cannot use them.
Four units, each roughly a thousand times the last: kilobyte, megabyte, gigabyte, terabyte.
Then the anchor sizes, and I want you to memorise these four because you cannot estimate
anything without them. A page of text is about fifty kilobytes. A photo is about four
megabytes. A song is about five megabytes. An hour of video is about two gigabytes.
Now the method, which is four steps. List and count — how many of each kind of file, and be
specific; "lots of photos" is not a number. Multiply count by typical size, one line per kind
of file. Convert everything to the same unit before you add, because that is where the
arithmetic goes wrong. And add the backup, which doubles the figure.
Work through the example at the bottom with me. Five hundred photos at four megabytes is
about two gigabytes. Two hundred songs is about one gigabyte. Ten hours of video at two
gigabytes an hour is twenty. Total, about twenty-three gigabytes — so a thirty-two gigabyte
drive looks fine until you remember the backup copy, and then it is not.

## Slide 7
PRACTICE ACTIVITIES
7
What you do in this lesson
Both activities are formative: you do them, you discuss them and you get written feedback, but they carry no marks. The marks for this topic are all in the Checkpoint.
Activity 1 — Specify a lab
Choose the monitors and one printer for a 25-seat computer lab. Give the specification and the reason for each choice, including the cost per page of the printer. The reasons carry the lesson, not the brand names.
Activity 2 — Storage maths
You are given a list of files with their sizes. Calculate the total, convert between units, and recommend which storage type fits — including one backup copy. Show the working, not only the answer.
Both activities are rehearsals for the marked task, which asks the same thinking about a whole machine.
Notes: Both activities here are rehearsals for the marked task, so treat them that way.
Activity one: twenty-five seats, a printer, and reasons. It is a lit classroom with a lot of
text printing, so the answers on slide three point one way — but I want the reason written
down, not the brand name. A specification with no reasons earns nothing, because anybody can
copy a specification off a website.
Activity two is the four-step method from slide six, applied to a list I will give you. Show
the working. If the arithmetic goes wrong but the method is visible, that is a conversation.
If only the answer is there, there is nothing to talk about.
And do not forget the backup copy. Every year somebody recommends a drive that fits the files
exactly, which means it fits the files and nothing else.

## Slide 8
KNOWLEDGE CHECK
8
Before you move on
Answer these three out loud. If any of them stalls you, go back to that slide.
1
Why does a cheap laptop with an SSD often feel faster than an expensive one with a hard drive?
2
A learner has 300 photos, 40 hours of video and a folder of documents. Roughly how much storage, with a backup?
3
A machine has plenty of free disk space but slows to a crawl with ten programs open. Which component is short, and why does disk space not help?
The Checkpoint quiz covers all three lessons and gives feedback after every answer.
Notes: Question one: the SSD has no moving parts and reaches data far faster, and most of what makes
a machine feel slow is waiting for the drive rather than waiting for the processor.
Question two: three hundred photos at four megabytes is about one point two gigabytes. Forty
hours of video at two gigabytes an hour is eighty. Documents are negligible next to that. So
roughly eighty-one gigabytes, and about a hundred and sixty with a backup. Notice that the
video swamps everything else — that is the real lesson of the question.
Question three is the RAM and storage distinction from slide four, and it is the one that
catches people. The machine is short of RAM, not disk space. Free space in the drawers does
not make the desk any bigger.

## Slide 9
LESSON COMPLETE
What to take with you
Softcopy vs hardcopy
output you can only see, and output you can hold.
Three numbers
GHz is how fast it thinks, cores is how many at once, GB of RAM is how much stays open.
RAM vs storage
the desk and the drawers. Short of RAM is why a machine crawls.
Estimate properly
count, multiply, convert, then double it for the backup.
Next up · Lesson 3: Connecting devices, health and environment, authentication
9
Notes: Softcopy and hardcopy, the three numbers on a spec sheet, the desk-and-drawers picture of RAM
and storage, and the four-step way to estimate capacity — ending with doubling it for the
backup.
Next is the last content lesson of the course: how everything plugs together, what to do when
a device is not recognised, how to work at a computer without wrecking your neck or the
planet, and how you prove to a machine that you are you.